## Slide 1: How(UAVs) are used in Disaster Management

## Slide 2: What is UAV?
UAV (Unmanned Aerial Vehicle):
Is a type of an aircraft that operates with out human pilot on board. UAV can be remote controlled aircraft, or can fly autonomously based on preprogrammed flight plan.

## Slide 3: Flight planning
Remotely controlled
Autonomous

## Slide 4: Types of UAV
Rotary wings
Uses 2 or more rotating blades that revolve around fixed mast to generate the lift

## Slide 5: Fixed wing: Uses a fixed wing like normal airplane to provide the lift

## Slide 6: UAV Specification
eBee Plus SenseFly UAV
1.1 kg weight
Wingspan 110cm
3 km radio link range
45 minute maximum flight time
Payload consists of sensors, wireless communication equipment, RTK/PPK system for positioning (accuracy 3-5cm)

## Slide 7: Mapping Sensors
1-Digital Camera
Used for day operation they include video camera and high definition photographic equipment.

## Slide 8
2- Infrared sensors:
They are used for night vision, and heat sensing.

## Slide 9: 3-Light Detection And Ranging (LiDAR)
A surveying tool used for creating point cloud and digital elevation models of the ground.
(Point cloud is a set of data points in 3D coordinates, represents the external surface of the object)

## Slide 10: UAV photogrammetric products include:
DSM / DTM (3D Models)
Orthophoto (geospatially corrected aerial images)
Contour Plans
Topographic Maps
High definition Digital Images.

## Slide 11: UAV photogrammetric products
Orthophoto
Digital Terrain Model (DTM) Digital Surface Model (DSM)
Contour Line Plan
3D Model

## Slide 12: Four phases of Disaster Management

## Slide 13: UAV Application in Disaster Management

## Slide 14: UAVs – Preparedness
UAVs can assist in many areas of pre-disaster preparedness and planning:
* Mapping, determining hazard areas, evacuation routes and safe zones
* Determine locations for pre-placement and deployment of resources
* Preplanning and familiarization for tactical and strategic responses
* Support of training and exercise activities

## Slide 15: UAVs - Response
UAVs can support many missions during the Response Phase of a disaster including:
* Provide real time situational awareness including locations of threats and hazards
* Survey damaged or assess conditions in inaccessible disaster areas
* Determine status of roads and critical infrastructure
* Provide geospatial references and navigation
* Monitor response operations and its effectiveness
* Assist Search and Rescue Operations

## Slide 16: UAVs - Recovery
The Recovery Phase is historically the longest phase of a disaster response:
* Survey damaged areas and structures
* Provide geospatial references and navigation
* Determine status of roads and critical infrastructure
* Monitor recovery operations and effectiveness
* Monitor the movement of persons, vehicles and resources
* Provide support for security operations

## Slide 17: UAVs - Mitigation
*UAVs have many applications that can assist authorities in mitigation efforts:
* Surveying new land for settlement
* Monitoring snow melt, storm runoff to prevent flooding
* Determine status of transportation routes
* preparation of maps and documents for pre-disaster conditions.

## Slide 18: Conclusion
- UAVs can save lives, property,
- UAVs are a reasonably low cost solution for disaster management
- UAV data are used to create 3D models, when compared with historical data, offers new perspectives of the extent of the damage.
- UAV data are used in planning, construction for new settlements.

## Slide 19
THANK YOU